# Market

DOT

# Challenge

A 42” concrete culvert’s joints had become separated and offset resulting in erosion of the surrounding

soil. One joint was separated enough and the erosion was so severe that sunlight was entering the culvert. The concern was that the above road would soon become threatened if the erosion continued unchecked.

# Engineered Solution

Four Extra-Wide and Six Double-Wide HydraTite Internal Pipe Joint Seals were the chosen solution.

The Double-Wide seals’ larger width would accommodate the joints with more severe separation and offset.

# Scope

The culvert had been cleaned out previously, but recent rain had covered the invert in new debris. The

debris was cleaned off of each joint and the ten seals were installed. The entire project was completed in only three days.

# Solution

HydraTite enables a trenchless repair at a fraction of the cost of fully lining the pipeline or excavation.

The sealed joints eliminated erosion and protected the above road. The job was done quickly and without disruption to traffic.