# Market

Industrial

# Challenge

An active mine had diverted the flow of water over a 10-foot by 6-foot box-shaped tunnel

and the water had found its way into a joint. The resulting leak threatened the limestone conveyer that ran through the center of the tunnel. The infiltrating water caused production and maintenance issues and a solution to eliminating the infiltration was needed quickly. The chosen solution needed to be implemented around the conveyor without disassembly and the existing piping and conduit would have to be worked around as well.

# Engineered Solution

The proposed solution utilized an extra-wide HydraTite Internal Pipe Joint Seal.

# Scope

The conveyer was locked out and supports for the piping and conduit were removed to

provide clearance from the wall. Prior to HydraTech’s involvement, repair attempts had been made, leaving the surface uneven and so it needed to be ground down in preparation for the HydraTite Seal installation. The extra-wide EPDM rubber seal then was placed around the conveyer and cold bonded on-site. The shape of the tunnel allowed for installation without corner forms which are frequently required for these types of installations. Despite the challenge of bonding the seal in the field, the entire job was completed, prep to finish, in 60 hours (2 days).

# Solution

HydraTite proved to be the flexible solution that was customizable enough for installation

around an immovable conveyer. The project was completed quickly and economically, protecting the conveyer for years to come.

https://hydratechllc.com/services/field-services/