Market: DOT

Challenge:

The Hopple Street bridge above I-75 needed to be strengthened to an appropriate capacity. The project required complex traffic control and challenging height access.

Engineered Solution:

Carbon fiber wrap was the chosen technology for structurally rehabilitating the existing bridge. The FRP technology increased the bridge’s shear strength.

Scope:

The project required nightly lane closures and a hydraulic lift to access parts of the supporting structure that were up to 50 above the interstate. The surfaces were prepared by pressure washing and grinding. Multiple layers of carbon layers were applied onto specific pier caps sections in a continuous form. The process was completed in a two week period.

Solution:

The application of fiber wrap reinforcement renewed the integrity of the Hopple Street bridge. It proved to be a flexible solution that allowed mobilization and demobilization, only effecting the traffic at night on this congested section of interstate. The project was completed in a fraction of the time and at a portion of the cost required by other repair and reinforcement methods.

HydraTech Engineered Products, LLC
HydraTech Field Services, LLC
10448 Chester Road, Cincinnati, Ohio 45215 Phone: (513) 827-9169 Fax: (513) 827-9171 http://www.hydratechllc.com https://www.hydratechfs.com