Market

Water Treatment Plant

Challenge

A large-diameter supply aqueduct located under a historic reservoir was inspected and infiltration was

documented at many of the pipe joints. The project required a small window for the system to be out of service and the aqueduct could not be fully drained due to the infiltration into the pipe system.

Engineered Solution     
The HydraTite Internal Pipe Joint Seal was selected for its ability to promptly eliminate leakage during a limited work window, and its capacity of being installed over joints with active leaks.

Scope

Once the pipe was shut down, an inspection of the piping took place and a schedule was developed to

prioritize the joints. HydraTech was then tasked with manufacturing the seals to the uncommon

diameter of 117.5”. At the time of repair, the leakage was found to be more severe than originally

expected so the number of seals was doubled. HydraTech manufactured and installed all seals

on schedule.

Solution

The HydraTite seals eliminated infiltration at all joints and installation was completed during the three-week window. The HydraTite solution enables a trenchless repair at a fraction of the cost of alternatives. The HydraTite seal proved to be an economical in situ repair solution that made the operation of the aqueduct more cost-effective.

HydraTech Engineered Products, LLC

HydraTech Field Services, LLC
10448 Chester Road Cincinnati, Ohio 45215      Phone: (513) 827-9169      Fax: (513) 8279171

https://hydratechllc.com

https://hydratechllc.com/services/field-services/