Market:

Gas Pipeline – North Texas Region

Challenge:

The customer was experiencing external corrosion on a buried transmission pipe as a result of coating failure. They requested a solution to eliminate the external corrosion and structurally renew the pipe system to its original design conditions.

Engineered Solution:

The HydraWrap® pipe wrap repair system was selected. The HydraWrap® repair system is an engineered product that provides a cost effective repair solution with a proven history of quality repairs. HydraWrap® protects against corrosion and reinforcing strength.

Scope:

A long-term repair solution was requested to repair corrosion anomalies at seventy-one dig site locations. This process would include structural rehabilitation of the pipeline from its current condition to the original design specifications by using the HydraWrap® carbon fiber reinforcements system.

Solution:

Each location was media blasted to SSPC-SP10 / NACE 2 near white specifications. Individual assessments were performed on identified anomalies. Each anomaly was repaired according to the direction provided by HydraTech engineers. The HydraWrap® system utilized bidirectional carbon fiber fabric and proprietary 100% solid epoxies which provided a long term cost effective solution for the client’s pipeline repairs. Two separate areas of the 14-in pipe were repaired and reinforced with the HydraWrap® carbon fiber reinforced composite. The HydraWrap® system restored the structural integrity and extended the service life of the pipe.

HydraTech Engineered Products, LLC

HydraTech Field Services, LLC

10448 Chester Road, Cincinnati, Ohio 45215    Phone: (513) 827-9169    Fax: (513) 827-9171 http://www.hydratechllc.com

https://www.hydratechfs.com