Market:

Water Treatment Plant

Challenge:

A section of piping that was immersed in a treatment tank had several deteriorated areas that required repair.

Engineered Solution:

The solution utilized the HydraWrap® Structural Composite Repair System, as well as the NSF61 8001 Waterline Epoxy.

Scope:

The customer requested that the pipe system be reinforced and brought back to its original design condition and that the repair be made with a very quick turnaround.

Solution:

The HydraWrap® composite repair was designed to reinforce an 8″ diameter carbon steel supply pipe with a maximum design pressure of 90 psi. The design of the HydraWrap® was based on limiting the strain in the composite repair to the allowable strains recommended by ASME. After applying the HydraWrap® system to the pipe, the composite repair was top coated with HydraTech’s NSF61 8001 Waterline epoxy. The project took less than a week to complete.

HydraTech Engineered Products, LLC

HydraTech Field Services, LLC

10448 Chester Road, Cincinnati, Ohio 45215    Phone: (513) 827-9169    Fax: (513) 827-9171 http://www.hydratechllc.com

https://www.hydratechfs.com