Products:

Market:

Power

Challenge:

Repairs were required in four 77.5-in circulating water box expansion joints and two circulating water pump expansion joints.

Engineered Solution:

The HydraTite® seal was proposed as a solution. HydraLine was to be applied prior to the seal's installation.

Scope:

Engineers walked down the project to review drawings and system operating parameters. They provided the solution of utilizing the HydraTite® seal with three two-piece 316L stainless steel bands, an extra wide HydraTite® seal, and a 16 gauge stainless steel backing plate to provide an internal slip joint repair. Prior to the seal's installation, HydraLine was applied to the interior surface of the pipe near the joint to create a unified and smooth substrate.

Solution:

The crew and all materials entered through an existing manhole and were able to complete the system installation within the work window, providing significant savings over traditional replacement of the expansion joints.

HydraTech Engineered Products, LLC

HydraTech Field Services, LLC

10448 Chester Road, Cincinnati Ohio 45215      Phone: (513) 827-9168      Fax: (513) 827-9171

https://hydratechllc.com

https://hydratechllc.com/services/field-services/